## Slide 1
Design of a hardware Root-of-Trust
on embedded systems
Eros Camacho-Ruiz
Supervisors:
Dr. Piedad Brox Jiménez
Prof. Francisco Vidal Fernández Fernández
Sevilla, March 13th 2024
Notes: [0] In order to increase the security in electronic devices, Physical Unclonable Functions (PUF) appear as an alternative to traditional non-volatile memories.
[1] PUFs compute a function which is unique for each device and unpredictable that is not possible to anticipate the response. Also, the PUF should be reliable that is the same response for the same challenge applied to the same instance.
[2] The variability of the manufacturing process of integrated circuits plays a special role in this PUFs due to uniqueness and unpredictability.
[3] This work is focused on the use of Static Random Access Memory (SRAM) cells as building components of the PUF. Very popular in electronic devices as fingerprint identifier.
[4] One of the most used topologies is the 6T cell.
Two data-holding cross-coupled inverters (transistors M1-M4) form the SRAM core (with "Q "and Q ̅ as input/output nodes). Another two transistors, M5 and M6, allow access (to write and read information) through the bit-lines (BL and (BL) ̅) when the word-line (WL) is active.
The response of an SRAM PUF, which is built from a collection of SRAM cells, is given by the power-up voltage values of these cells. Due to process variations during fabrication, an unbalance in the threshold voltages of the core transistors usually occur. When this happens, node "Q" sets at either a logic value “1” or “0” when the cell is powered-up. The challenge then is the powering up of the cells and the response is the collective power-up values. Ideally, the cells within an SRAM PUF would be stable. In this context, a stable SRAM cell means that it always powers up to the same state. However, although factors like electrical noise can change the power-up value from one iteration to another, cells are not equally affected by these factors. There are different techniques to improve the PUF reliability that consist in characterizing the stability of each cell so that only the most stable cells are used. The Multiple Evaluation method, for instance, uses multiple power-ups [5][6] to discriminate between stable and unstable cells. Other methods [7][8] rely on the concept of Data Retention Voltage (DRV) to identify stable cells. That value is the minimum supply voltage in a SRAM cell for which the logic values can be stored safely and reliably. More specifically, the Maximum Trip Supply Voltage (MTSV) method [7] correlates the value of DRV to the degree of stability of each SRAM cell.
The goal of this paper is to corroborate the experimental findings in [7] but using simulation this time around: i.e., to demonstrate that the MTSV method can indeed identify stability and thus improve the PUF reliability. This will be done using the concept of Static Noise Margin (SNM) [9]-[11] of the two data-holding inverters. The SNM can be interpreted as the maximum amount of noise that the SRAM can tolerate without changing its state (from “1” to “0”, or vice versa). The SNMs are calculated from the butterfly curve generated from the voltage transfer characteristic (VTC) of each inverter. As VDD is raised from 0V to its nominal value during the power-up, the butterfly curve evolves (as it will be shown later) and so does the value of the SNMs. This can be used to relate the DRV used by the MTSV metric with the SNM.

## Slide 2: Introduction
2
Critical Infraestructure
Data privacy preserving
Economic and National Security Implications
Global Communications
Cybersecurity
Information security
Notes: [0] In order to increase the security in electronic devices, Physical Unclonable Functions (PUF) appear as an alternative to traditional non-volatile memories.
[1] PUFs compute a function which is unique for each device and unpredictable that is not possible to anticipate the response. Also, the PUF should be reliable that is the same response for the same challenge applied to the same instance.
[2] The variability of the manufacturing process of integrated circuits plays a special role in this PUFs due to uniqueness and unpredictability.
[3] This work is focused on the use of Static Random Access Memory (SRAM) cells as building components of the PUF. Very popular in electronic devices as fingerprint identifier.
[4] One of the most used topologies is the 6T cell.
Two data-holding cross-coupled inverters (transistors M1-M4) form the SRAM core (with "Q "and Q ̅ as input/output nodes). Another two transistors, M5 and M6, allow access (to write and read information) through the bit-lines (BL and (BL) ̅) when the word-line (WL) is active.
The response of an SRAM PUF, which is built from a collection of SRAM cells, is given by the power-up voltage values of these cells. Due to process variations during fabrication, an unbalance in the threshold voltages of the core transistors usually occur. When this happens, node "Q" sets at either a logic value “1” or “0” when the cell is powered-up. The challenge then is the powering up of the cells and the response is the collective power-up values. Ideally, the cells within an SRAM PUF would be stable. In this context, a stable SRAM cell means that it always powers up to the same state. However, although factors like electrical noise can change the power-up value from one iteration to another, cells are not equally affected by these factors. There are different techniques to improve the PUF reliability that consist in characterizing the stability of each cell so that only the most stable cells are used. The Multiple Evaluation method, for instance, uses multiple power-ups [5][6] to discriminate between stable and unstable cells. Other methods [7][8] rely on the concept of Data Retention Voltage (DRV) to identify stable cells. That value is the minimum supply voltage in a SRAM cell for which the logic values can be stored safely and reliably. More specifically, the Maximum Trip Supply Voltage (MTSV) method [7] correlates the value of DRV to the degree of stability of each SRAM cell.
The goal of this paper is to corroborate the experimental findings in [7] but using simulation this time around: i.e., to demonstrate that the MTSV method can indeed identify stability and thus improve the PUF reliability. This will be done using the concept of Static Noise Margin (SNM) [9]-[11] of the two data-holding inverters. The SNM can be interpreted as the maximum amount of noise that the SRAM can tolerate without changing its state (from “1” to “0”, or vice versa). The SNMs are calculated from the butterfly curve generated from the voltage transfer characteristic (VTC) of each inverter. As VDD is raised from 0V to its nominal value during the power-up, the butterfly curve evolves (as it will be shown later) and so does the value of the SNMs. This can be used to relate the DRV used by the MTSV metric with the SNM.

## Slide 3: Introduction
3
Hypothesis
Contributing to improve the security of information using hardware solutions in IoT environments where restrictions are usually stronger.
How ?
Proposing a Root-of-Trust composed of different modules that have been designed separately.
Use Cases to demonstrate the feasibility of the dissertation

## Slide 4: Overview
4
Dissertation
Structure
RTN-based PUF
Hash Functions
Evaluation
Analog low-level design
SHA-2
RTL design
Digital low-level design
SHA-3
RTL design
PQC
NTRU
PoC
HMAC
NTRU

## Slide 5: What is a PUF ?
5
Physical Unclonable Function (PUF)
INPUT
Challenge
OUTPUT
Response
PUF
Key Obfuscation
Device identification
Notes: [0] In order to increase the security in electronic devices, Physical Unclonable Functions (PUF) appear as an alternative to traditional non-volatile memories.
[1] PUFs compute a function which is unique for each device and unpredictable that is not possible to anticipate the response. Also, the PUF should be reliable that is the same response for the same challenge applied to the same instance.
[2] The variability of the manufacturing process of integrated circuits plays a special role in this PUFs due to uniqueness and unpredictability.
[3] This work is focused on the use of Static Random Access Memory (SRAM) cells as building components of the PUF. Very popular in electronic devices as fingerprint identifier.
[4] One of the most used topologies is the 6T cell.
Two data-holding cross-coupled inverters (transistors M1-M4) form the SRAM core (with "Q "and Q ̅ as input/output nodes). Another two transistors, M5 and M6, allow access (to write and read information) through the bit-lines (BL and (BL) ̅) when the word-line (WL) is active.
The response of an SRAM PUF, which is built from a collection of SRAM cells, is given by the power-up voltage values of these cells. Due to process variations during fabrication, an unbalance in the threshold voltages of the core transistors usually occur. When this happens, node "Q" sets at either a logic value “1” or “0” when the cell is powered-up. The challenge then is the powering up of the cells and the response is the collective power-up values. Ideally, the cells within an SRAM PUF would be stable. In this context, a stable SRAM cell means that it always powers up to the same state. However, although factors like electrical noise can change the power-up value from one iteration to another, cells are not equally affected by these factors. There are different techniques to improve the PUF reliability that consist in characterizing the stability of each cell so that only the most stable cells are used. The Multiple Evaluation method, for instance, uses multiple power-ups [5][6] to discriminate between stable and unstable cells. Other methods [7][8] rely on the concept of Data Retention Voltage (DRV) to identify stable cells. That value is the minimum supply voltage in a SRAM cell for which the logic values can be stored safely and reliably. More specifically, the Maximum Trip Supply Voltage (MTSV) method [7] correlates the value of DRV to the degree of stability of each SRAM cell.
The goal of this paper is to corroborate the experimental findings in [7] but using simulation this time around: i.e., to demonstrate that the MTSV method can indeed identify stability and thus improve the PUF reliability. This will be done using the concept of Static Noise Margin (SNM) [9]-[11] of the two data-holding inverters. The SNM can be interpreted as the maximum amount of noise that the SRAM can tolerate without changing its state (from “1” to “0”, or vice versa). The SNMs are calculated from the butterfly curve generated from the voltage transfer characteristic (VTC) of each inverter. As VDD is raised from 0V to its nominal value during the power-up, the butterfly curve evolves (as it will be shown later) and so does the value of the SNMs. This can be used to relate the DRV used by the MTSV metric with the SNM.

## Slide 6: What is a PUF ?
6
Unique
Unpredictable
Response Characteristics
Reliable
Notes: [0] In order to increase the security in electronic devices, Physical Unclonable Functions (PUF) appear as an alternative to traditional non-volatile memories.
[1] PUFs compute a function which is unique for each device and unpredictable that is not possible to anticipate the response. Also, the PUF should be reliable that is the same response for the same challenge applied to the same instance.
[2] The variability of the manufacturing process of integrated circuits plays a special role in this PUFs due to uniqueness and unpredictability.
[3] This work is focused on the use of Static Random Access Memory (SRAM) cells as building components of the PUF. Very popular in electronic devices as fingerprint identifier.
[4] One of the most used topologies is the 6T cell.
Two data-holding cross-coupled inverters (transistors M1-M4) form the SRAM core (with "Q "and Q ̅ as input/output nodes). Another two transistors, M5 and M6, allow access (to write and read information) through the bit-lines (BL and (BL) ̅) when the word-line (WL) is active.
The response of an SRAM PUF, which is built from a collection of SRAM cells, is given by the power-up voltage values of these cells. Due to process variations during fabrication, an unbalance in the threshold voltages of the core transistors usually occur. When this happens, node "Q" sets at either a logic value “1” or “0” when the cell is powered-up. The challenge then is the powering up of the cells and the response is the collective power-up values. Ideally, the cells within an SRAM PUF would be stable. In this context, a stable SRAM cell means that it always powers up to the same state. However, although factors like electrical noise can change the power-up value from one iteration to another, cells are not equally affected by these factors. There are different techniques to improve the PUF reliability that consist in characterizing the stability of each cell so that only the most stable cells are used. The Multiple Evaluation method, for instance, uses multiple power-ups [5][6] to discriminate between stable and unstable cells. Other methods [7][8] rely on the concept of Data Retention Voltage (DRV) to identify stable cells. That value is the minimum supply voltage in a SRAM cell for which the logic values can be stored safely and reliably. More specifically, the Maximum Trip Supply Voltage (MTSV) method [7] correlates the value of DRV to the degree of stability of each SRAM cell.
The goal of this paper is to corroborate the experimental findings in [7] but using simulation this time around: i.e., to demonstrate that the MTSV method can indeed identify stability and thus improve the PUF reliability. This will be done using the concept of Static Noise Margin (SNM) [9]-[11] of the two data-holding inverters. The SNM can be interpreted as the maximum amount of noise that the SRAM can tolerate without changing its state (from “1” to “0”, or vice versa). The SNMs are calculated from the butterfly curve generated from the voltage transfer characteristic (VTC) of each inverter. As VDD is raised from 0V to its nominal value during the power-up, the butterfly curve evolves (as it will be shown later) and so does the value of the SNMs. This can be used to relate the DRV used by the MTSV metric with the SNM.

## Slide 7: A novel RTN-based PUF
7
Random Telegraph Noise (RTN)
Low biasing voltages  Prevent aging
Maximum Parameter Fluctuation
(MPF)
Cumulative difference between the maximum and the minimum in a time interval of a drain
CURRENT / VOLTAGE trace
Handle the RTN
Patent: WO/2023/202843
MÉTODO Y DISPOSITIVO PARA FUNCIÓN FÍSICA NO CLONABLE (PUF) BASADA EN RUIDO TELEGRÁFICO ALEATORIO (RTN)

## Slide 8: A novel RTN-based PUF: Schematic
8
MPF
Current/Voltage trace with RTN
Pair of transistors
1-bit Response = {0,1}
Current/Voltage trace with RTN
MPF
Comparison

## Slide 9: A novel RTN-based PUF: Architecture
9
Architecture
Single
Differential
VOLTAGE
CURRENT
VOLTAGE
CURRENT

## Slide 10: A novel RTN-based PUF: Metrics
10
Probability
Number of zeros/ones → /
Number of measurements →
Bit Selection Method
Reliability (1-HDIntra)
Metrics
Uniqueness (HDInter)
Unpredictability (HW)
Probability (P)

## Slide 11: A novel RTN-based PUF: Evaluation
11
Evaluation
Is it feasible to build a PUF based on RTN?
How sizes and biasing conditions can alter the PUF performance?
How non-idealities of the circuitry needed to get the response can affect the PUF performance?
Low-level design
Differential Current mode

## Slide 12: A novel RTN-based PUF: Evaluation #1
12
Is it possible to obtain a reliable response from this PUF?
 | [7] Mispan, IEEE Prime 2015 | [8] Mispan, IOLTS 2016 | [9] Zhuang, IEEE TCAS I, 2020 | This diss.
Reliability (%) | 91.58 | - | 94.2 | 99.8
HDinter (%) | 50.23 | 49.9 | 49.9 | 49.99
HW (%) | - | 53.94 | 53.94 | 50.09
Comparing with similar area PUFs
32-bit response
Comparing with similar quality metrics PUFs
 | [14] Yoshinaga ISCAS 2016 | [12] Santana-Andreo, Integration, 2022 | This diss.
Reliability (%) | 99.99 | 99.99 | 99.99
HDinter (%) | 48.0 | - | 49.97
HW (%) | - | 50 | 49.96
Technology | 65-nm | 65-nm | 65-nm
Number of transistors | 34,816 (2,048 17T-ROs) | 4,992 (832 6T-SRAM cells) | 2,286
128-bit response

## Slide 13: A novel RTN-based PUF: Evaluation #2
13
How sizes and biasing conditions can alter the PUF performance?
OPTIMUM SIZE
80x60 nm2
OPTIMUM BIASING
&
Larger Transistors
Stable Pairs
 Smaller Transistors
 Area Cost per Bit

## Slide 14: A novel RTN-based PUF: Evaluation #3
14
How non-idealities of the circuitry needed to get the response can affect the PUF performance?
MCF Extractor and Comparator must be carefully designed
Non-idealities of the circuitry can affect the performance of the PUF
The on-resistance and off-resistance of the transistor selector can affect the performance

## Slide 15: Low-level design of the RTN-based PUF
15
Evaluation
Low-level design
Differential Voltage mode
Avoiding potential issues in current sensing
Examination of different ICC in CC method can improve the PUF quality.
In case aging impacts the PUF, adjusting voltage levels is a simple task.
Analog design flow

## Slide 16: Low-level design: floorplan
16

## Slide 17: Low-level design: array design
17
4,096 transistors
OPTIMUM SIZE
L = 100nm
W = 2um
tmin = 10us

## Slide 18: Low-level design: ASB design
18
Circuit | Static Error (mV) | 
 | µ | σ
PDHMAX | 0.5319 | 0.141
PDHMIN | 0.8405 | 0.250
PDH design

## Slide 19: Low-level design: ASB design
19
Substractor design

## Slide 20: Low-level design: ASB design
20
Comparator design

## Slide 21: Low-level design: ASB design
21

## Slide 22: Low-level design: Milestone - I
22

## Slide 23: Hash Functions
23
Hash Functions
Verification of message integrity
Signature generation and verification
Password hashing
Key derivation
Collision Resistance
Preimage resistance
Second Preimage resistance
NIST
SHA-2
SHA-3

## Slide 24: Hash Functions
24
Competitive trade-off between time and area
Comparison with the SATO
Desing of a highly configurable IP: AXI4-Lite
ASIC implementation of the SHA-256
Drivers to use the IP module

## Slide 25: SHA-2
25
Message Schedule
SHA-2 Core

## Slide 26: SHA-2
26
SHA-2 IP

## Slide 27: SHA-2
27
Ref | Platform | SHA-2 ver. | Area | Frequency | Throughput | Efficiency
 |  |  | (Slices) | (MHz) | (Gbps) | (Mbps/Slice)
[89] | Virtex | SHA-256 | 755 | 174.00 | 1.370 | 1.830
[90] | Virtex | SHA-256 | 6136 | 35.10 | 2.077 | 0.338
[91] | Virtex-5 | SHA-256 | 387 | 202.54 | 1.580 | 4.190
[92] | Virtex-4 | SHA-256 | 610 | 170.75 | 1.345 | 2.200
[93] | Virtex-5 | SHA-256 | 1895 | 411.30 | 3.290 | 1.740
This diss. | Virtex-7 | SHA-256 | 282 | 191.13 | 1.630 | 5.784
[89] | Virtex | SHA-512 | 1667 | 141.00 | 1.780 | 1.010
[91] | Virtex-5 | SHA-512 | 874 | 176.06 | 2.200 | 2.580
[94] | Virtex-5 | SHA-512 | 1080 | 129.00 | 0.826 | 0.765
This diss. | Virtex-7 | SHA-512 | 576 | 173.52 | 2.221 | 3.856

## Slide 28: SHA-2
28
SHA-2 IP Interface
SHA-2 | Message Length | Throughput
Instance | < Block Size | > Block Size
SHA-224 | x0.68 | x0.87
SHA-256 | x0.67 | x0.87
SHA-384 | x1.54 | x2.35
SHA-512 | x1.44 | x2.32
SHA-512/224 | x1.64 | x2.35
SHA-512/256 | x1.64 | x2.37

## Slide 29: SHA-256 low-level design
29
Low-level design
RTL design
Digital design flow
Inferring registers and memory cells instead of BRAMs.
Adding an interface
SHA-256
Modifications

## Slide 30: SHA-256 low-level design
30
Low-level schematic
Occupation
Layout
Module | Cell Count (GE) | Cell Area(µm2) | Net Area(µm2) | Total Area(µm2)
SIPO | 261 | 1317.240 | 742.423 | 2059.663
PISO | 516 | 2507.400 | 1479.523 | 3986.923
Control | 52 | 181.440 | 2594.252 | 2775.692
SHA-256 (Core) | 19350 | 118787.400 | 70292.775 | 189080.175
Total | 20179 | 122793.480 | 75108.973 | 197902.453

## Slide 31: SHA-256 low-level design tests
31
NIST Test Vector

## Slide 32: SHA-3
32
SHA-3 family has relatively fewer implementation costs and is much faster
SHA-3 family is noted as PQC primitive
SHA-3 is based in the Keccak algorithm
NIST
SHA-2
SHA-3

## Slide 33: SHA-3
33
Basic version
Opt. #1
Opt. #2

## Slide 34: SHA-3
34
SHA-3 IP

## Slide 35: SHA-3
35
Ref | Platform | SHA-3 ver. | Area | Throughput | Efficiency
 |  |  | (Slices) | (Gbps) | (Mbps/Slice)
[88] | Virtex-6 | SHA3-512 | 1406 | 16.51 | 11.47
[107] | Virtex-6 | SHA3-512 | 2296 | 18.78 | 8.17
[110] | Virtex-5 | SHA3-512 | 1163 | 7.80 | 6.06
This diss. | Virtex-7 | SHA3-512 | 1456 | 17.97 | 12.34
[109] | Virtex-7 | SHA3-256 | 1618 | 20.08 | 12.90
[108] | Virtex-7 | SHA3-256 | 1418 | 14.30 | 11.97
This diss. | Virtex-7 | SHA3-256 | 1566 | 29.25 | 18.68
[111] | Zynq-7000 | SHA3-224 | 1424 | 12.8 | 8.98
This diss. | Zynq-7000 | SHA3-224 | 1577 | 30.00 | 19.02

## Slide 36: SHA-3
36
SHA-3 IP Interface
SHA-3 | Message Length | Throughput
Instance | < Block Size | > Block Size
SHA3-224 | x6.23 | x10.89
SHA3-256 | x6.41 | x11.71
SHA3-384 | x6.77 | x14.54
SHA3-512 | x7.33 | x19.93
SHAKE128 | x2.80 | x8.18
SHAKE256 | x3.07 | x9.64

## Slide 37: Post-Quantum Cryptography
37
Secret key Scheme
Public key Scheme
Grove Alg.
Shor Alg.
Quantum Computers

## Slide 38: Post-Quantum Cryptography
38
Grove Alg.
Shor Alg.
Post-Quantum Cryptography
Third Round
(2020)
Selected Algorithms
(2022)
First Draft
(2023)
NTRU
Implementing the polynomial multiplier in HW

## Slide 39: PQC: NTRU
39
NTRU (IEEE 1363.1)
Accelerating N cycles when a 0 is found in the blind polynomial
Can we use this strategy with NTRU Round-3 ?
The number of non-zeros of the blind polynomial is not constant
Disclosing information that has to be hided through timing attacks
New Strategy
Confident Limit
NTRU (Round-3)

## Slide 40: PQC: NTRU
40
Parallelization
strategy

## Slide 41: PQC: NTRU
41
IP Interface
N maxcoef | Max. Eff. | M | LUTs | FFs | BRAM | Acc. (x)
 | LUT | 4 | 285 | 119 | 4.5 | 20.67
400 | FF | 7 | 437 | 124 | 7.5 | 30.28
509 | BRAM | 8 | 584 | 205 | 4.5 | 32.81
 | LUT | 6 | 348 | 105 | 6.5 | 23.40
509 | FF | 7 | 399 | 106 | 7.5 | 26.00
 | BRAM | 8 | 556 | 187 | 4.5 | 28.35
 | LUT | 8 | 476 | 128 | 8.5 | 37.46
516 | FF | 10 | 582 | 133 | 10.5 | 43.08
677 | BRAM | 11 | 801 | 251 | 6.0 | 45.49
 | LUT | 8 | 451 | 108 | 8.5 | 31.23
677 | FF | 10 | 558 | 113 | 10.5 | 36.40
 | BRAM | 11 | 773 | 231 | 6.0 | 38.64
 | LUT | 8 | 510 | 129 | 8.5 | 40.06
625 | FF | 12 | 713 | 133 | 12.5 | 51.89
821 | BRAM | 13 | 981 | 287 | 7.0 | 54.25
 | LUT | 8 | 481 | 109 | 8.5 | 32.94
821 | FF | 12 | 679 | 113 | 12.5 | 43.74
 | BRAM | 13 | 929 | 267 | 7.0 | 45.99
 | LUT | 6 | 433 | 130 | 6.5 | 32.26
533 | FF | 10 | 634 | 133 | 10.5 | 43.54
701 | BRAM | 11 | 881 | 273 | 6.0 | 46.32
 | LUT | 6 | 403 | 110 | 6.5 | 25.52
701 | FF | 10 | 605 | 113 | 10.5 | 36.62
 | BRAM | 11 | 854 | 253 | 6.0 | 39.18

## Slide 42: PQC: NTRU SCA
42
Can that lead somehow to a leak of information ?
Single Power Analysis (SPA)
There is leakage of information
Applying countermeasures …

## Slide 43: PQC: NTRU SCA
43
First Countermeasure
Second Countermeasure

## Slide 44: PQC: NTRU SCA
44
Third Countermeasure
Not using 0’s in the multiplication operation
More closer …

## Slide 45: Proof-of-Concept
45
Root-of-Trust
Digital PUF
Digital TRNG
SHA2 / SHA3
NTRU accelerator
PoC
HMAC
NTRU
System-on-Chip (SoC)
IoT Environment
Combine modules in a RoT

## Slide 46: PoC: HMAC
46
Message Verification
HMAC

## Slide 47: PoC: NTRU
47
Improvement of the already presented
NTRU

## Slide 48: Conclusions
48
The establishment of a hardware RoT significantly bolsters the security of an embedded system. This enhancement is not only robust but also efficient, making it a critical component in the design of secure systems. The considerations for implementation within the framework of the IoT have led to a streamlined design of the RoT. This design is mindful of the constraints of IoT devices, particularly the size of transistors or the occupancy of logic resources in terms of FPGA implementations. The result is a compact yet powerful RoT that fits within the limited resources of IoT devices while providing robust security. In addition to the primary conclusion, there are several other insights extracted from this dissertation. These insights shed light on various aspects of the cryptosystem and contribute to our understanding of its design and implementation. They serve as valuable outcomes that can guide future research and development in this field. These conclusions are:

## Slide 49: Conclusions
49
1. Taking inspiration of the CIA triad as model designed to guide policies for information security, the design of a RoT that encompasses a set of crypto primitives is a suitable solution. The approach taken in this dissertation is primarily from a hardware-oriented perspective. This proposed RoT has included a PUF, which can be used as an identifier generator. They also incorporate hash functions, represented by SHA-2 and SHA-3, which are essential for ensuring data integrity. Moreover, it includes a cryptographic primitive that can securely accelerate the computation of PQC algorithms. One such PQC algorithm is NTRU, which is known for its security and efficiency. The integration of these components within a RoT provides a robust and secure hardware solution for addressing the principles of the CIA Triad in the IoT framework.

## Slide 50: Conclusions
50
2. The initial module developed in this dissertation was a PUF based on a typically undesirable phenomenon known as RTN. Several architectures were proposed in which, basically, the response of the PUF is obtained comparing one metric that encapsulate all the RTN information, the MPF. The initial stages involved designing and evaluating the PUF from a software perspective, which included conducting several simulations. Once positive results were obtained from these simulations, the next phase involved integrating this PUF into an ASIC. This process followed an analog design flow, culminating in the creation of the first silicon-based RTN-PUF, referred to as MILESTONE-I. The successful results of this endeavor led to the filing of an international patent.

## Slide 51: Conclusions
51
3. The following modules developed were those associated with hash functions. After studying the mathematical background of both selected hash functions (SHA-2 and SHA-3), the first step involved implementing the RTL in an FPGA. To this end, a comprehensive set of parameters was incorporated into the integration of these hash functions into IP modules, allowing the implementation of any of the hash versions collected in the standards. One of these designs, specifically SHA-256, was chosen for integration into an ASIC, following a fully digital design flow.

## Slide 52: Conclusions
52
4. The final module that was developed was related to the acceleration of one of the
algorithms selected by NIST in the third round of the PQC contest: the NTRU. In that algorithm, the critical component is the polynomial multiplication. To address this, a RTL design was developed, incorporating all the parameter sets outlined in the documentation. Consideration was given not only to performance but also to potential information leakage associated with timing and power attacks. The results demonstrated that it is feasible to enhance the speed of the algorithm while adding an additional layer of security against SCAs.

## Slide 53: Conclusions
53
5. Lastly, a final design of the RoT was proposed, integrating all modules into a single hardware platform. This comprehensive design was evaluated in various scenarios, demonstrating the reusability of each module. The results were highly promising, underscoring the effectiveness of this integrated approach in enhancing the security and efficiency of the embedded systems.

## Slide 55: Introduction
55

## Slide 56: Introduction
56
https://www.enisa.europa.eu/publications/good-practices-for-security-of-iot-1/@@download/fullReport
https://www.enisa.europa.eu/publications/guidelines-for-securing-the-internet-of-things/@@download/fullReport

## Slide 57: Introduction
57
https://qubip.eu/

## Slide 58: Introduction
58

## Slide 59: PUF: Architecture
59

## Slide 60: PUF: Bit Selection Method and Metrics
60